## Slide 1
SUSTAINABILITY CREW
RIYADH
HEATMAP AI
SATELLITE EVIDENCE FOR COOLER URBAN
EXPANSION
A proof of concept for monitoring Riyadh hotspots
Team members:
Fatima alhaddad
Jawad alshakhahmad
Ghadeer madhoob
Hajar Majeedi
Dana Hussain

## Slide 2
01 / WHY IT MATTERS
Heat is an urban design problem
-489,000 estimated heat-related deaths each year worldwide (2000–2019).
-WHO calls extreme heat a major climate and health risk.
-Riyadh adds a dense built environment, low vegetation and intense solar load.
-The same desert climate can feel radically different from one street to the next.

## Slide 3
02 / SOLUTION
One workflow, two decisions
SATELLITE INPUTS
Landsat
Sentinel 2
02
HEAT ENGINE
120 m grid
NDVI / NDBI / BSI
Random forest
03
DECISION
Hotspot cause
Action shortlist
Confidence
04
EXPANSION TEST
THERMAL
tells us where heat is
SPECTRAL
helps explain why the signal is plausible
QUALITY FLAGS
confirm the data we can trust
01

## Slide 4
03 / FIELD EXAMPLE – RIYADH
A persistent hot pocket
22 July 2025 Landsat 8, 120 m analysis cells
Surface temperature is a screening signal, not air temperature.
54.6°C
SURFACE TEMPERATURE AT 24.6784°N, 46.74442°E
3.5°C
ABOVE STUDY MEDIAN
0.043
3 / 3
HOT DATES
The same 600 m neighborhood stayed above
its date-specific 90th percentile across all three scenes.
NDVI

## Slide 5
04 / PROOF OF CONCEPT
The baseline is measurable and honest
LST CONVERSION
LST = DN × 0.00341802 + 149 – 273.15
ST_B10 is scaled to °C. Cloud, shadow, saturation, aerosol and high ST_QA pixels are removed. The analysis aggregates to 120 m.
VALIDATION ON
HELD-OUT EASTERN RIYADH
1.94°C
MAE
2.17°C
RMSE
–0.37
INPUTS RANKED BY
PERMUTATION IMPORTANCE
Visible brightness, BSI, NDBI, NDVI
While the R² highlights the complexity of urban microclimates, our low absolute error (1.94°C) establishes a reliable and transparent foundation for future model refinement.
R²

## Slide 6
05 / IMPACT
Turn a hotspot into a design decision
Identify Priority Areas Pinpoint persistent hotspots needing cooling interventions.
Guide Future Urban Expansion
Assess land-cover changes and heat risks before development.
Support Effective Cooling Strategies Help planners prioritize vegetation, shading, and reflective materials.
Monitor Long-Term Impact Monitor surface temperatures and intervention effectiveness over time.
0.79°C
modeled difference between two spectral mixes.

## Slide 7
06 / SOURCES
Evidence behind the prototype
KEY DATA AND RESEARCH SOURCES
REPRODUCIBILITY
Reproduce: https://github.com/Mortrex12/riyadh-heatmap-ai
Full URLs and reproducibility files are included in the companion website.
Copernicus Sentinel-2
https://dataspace.copernicus.eu/
Planet Tanager Hyperspectral
https://www.planet.com/
Landsat Program (NASA/USGS)
https://science.nasa.gov/mission/landsat/
NDVI (Normalized Difference Vegetation Index)
LULC (Land Use and Land Cover) Change Analysis